Using the Java Messaging System
# Overview
Celtix provides a transport plug-in that enables endpoints to use Java Messaging System (JMS) queues and topics. Celtix’s JMS transport plug-in uses the Java Naming and Directory Interface (JNDI) to locate and obtain references to the JMS provider that brokers for the JMS destinations. Once Celtix has established a connection to a JMS provider, Celtix supports the passing of messages packaged as either a JMS ObjectMessage or a JMS TextMessage.
# WSDL Namespace
The WSDL extensions for defining a JMS endpoint are defined in the namespace http://celtix.objectweb.org/transports/jms. In order to use the JMS extensions you will need to add the line shown in Text 1 to the definitions element of your contract.
xmlns:jms="http://celtix.objectweb.org/transports/jms"

Text 1: JMS Extension Namespace
# Configuration Namespace
The Celtix JMS endpoint configuration properties are specified under the namespace http://celtix.objectweb.org/transports/jms. In order to use the JMS configuration properties you will need to add the line shown in Text 2 to the beans element of your configuration.
xmlns:jms="http://celtix.objectweb.org/transports/jms"

Text 2: JMS Properties Namespace
# Basic Endpoint Configuration
JMS endpoints need to know certain basic information about how to establish a connection to the proper destination. This information can be provided in one of two places:
- WSDL File
- Celtix Configuration
## Using WSDL
The JMS destination information is provided using the jms:address element and its child, the jms:JMSNamingProperties element. The jms:address element’s attributes specify the information needed to identify the JMS broker and the destination. The jms:JMSNamingProperties element specifies the Java properties used to connect to the JNDI service.
The address Element
The basic configuration for a JMS endpoint is done by using a jms:address element as the child of your service’s port element. The jms:address element uses the attributes described in Table 1 to configure the connection to the JMS broker.
Attribute	Description
destinationStyle	Specifies if the JMS destination is a JMS queue or a JMS topic.
jndiConnectionFactoryName	Specifies the JNDI name bound to the JMS connection factory to use when connecting to the JMS destination.
jndiDestinationName	Specifies the JNDI name bound to the JMS destination to which requests are sent.
jndiReplyDestinationName	Specifies the JNDI name bound to the JMS destinations where replies are sent. This attribute allows you to use a user defined destination for replies. For more details see Using a Named Reply Destination.
connectionUserName	Specifies the username to use when connecting to a JMS broker.
connectionPassword	Specifies the password to use when connecting to a JMS broker.

Table 1: JMS Endpoint Attributes
The JMSNamingProperties Element
To increase interoperability with JMS and JNDI providers, the jms:address element has a child element, jms:JMSNamingProperties, that allows you to specify the values used to populate the properties used when connecting to the JNDI provider. The jms:JMSNamingProperties element has two attributes: name and value. The name attribute specifies the name of the property to set. The value attribute specifies the value for the specified property. jms:JMSNamingProperties element can also be used for specification of provider specific properties.
The following is a list of common JNDI properties that can be set:
- java.naming.factory.initial
- java.naming.provider.url
- java.naming.factory.object
- java.naming.factory.state
- java.naming.factory.url.pkgs
- java.naming.dns.url
- java.naming.authoritative
- java.naming.batchsize
- java.naming.referral
- java.naming.security.protocol
- java.naming.security.authentication
- java.naming.security.principal
- java.naming.security.credentials
- java.naming.language
- java.naming.applet
For more details on what information to use in these attributes, check your JNDI provider’s documentation and consult the Java API reference material.
Using a Named Reply Destination
By default, Celtix endpoints using JMS create a temporary queue for sending replies back and forth. You can change this behavior by setting the jndiReplyDestinationName attribute in the endpoint's contract. A Celtix client endpoint will listen for replies on the specified destination and it will specify the value of the attribute in the ReplyTo field of all outgoing requests. A Celtix service endpoint will use the value of the jndiReplyDestinationName attribute as the location for placing replies if there is no destination specified in the request’s ReplyTo field.
Example
Text 3 shows an example of an Celtix JMS port specification.
<service name="JMSService"> / <port binding="tns:Greeter_SOAPBinding" name="SoapPort"> / <jms:address jndiConnectionFactoryName="ConnectionFactory" / jndiDestinationName="dynamicQueues/test.Celtix.jmstransport"> / <jms:JMSNamingProperty name="java.naming.factory.initial" / value="org.activemq.jndi.ActiveMQInitialContextFactory" /> / <jms:JMSNamingProperty name="java.naming.provider.url" / value="tcp://localhost:61616" /> / </jms:address> / </port> / </service>

Text 3: Celtix JMS Port
## Using Celtix Configuration
In addition to using the WSDL file to specify the connection information for a JMS endpoint, you can supply it in the endpoint's configuration file. The information in the configuration file will override the information in the endpoint's WSDL file.
JMS connection information is specified using the jmsAddress property. The jmsAddress property has a single value: jms:address. It is identical to the jms:address element used in the WSDL file. Its attributes are listed in Table 1. Like the jms:address element in the WSDL file, the jms:address property also has a jms:JMSNamingProperties child element that is used to specify additional information used to connect to a JNDI provider. For more information on populating this element see JMSNamingProperties.
The jmsAddress property can be specified in either the client configuration bean or the service configuration bean.
Example
Text 4 shows a Celtix configuration entry for configuring the addressing information for a JMS consumer endpoint.
<beans xmlns:ct="http://celtix.objectweb.org/configuration/types" / xmlns:jms="http://celtix.objectweb.org/transports/jms"> / ... / <bean id="celtix.{http://celtix.objectweb.org/jms_conf_test} / HelloWorldQueueBinMsgService/HelloWorldQueueBinMsgPort.jms-client" / class="org.objectweb.celtix.bus.transports.jms.jms_client_config.spring.JMSClientConfigBean"> / <property name="jmsAddress"> / <value> / <jms:address destinationStyle="queue" / jndiConnectionFactoryName="MockConnectionFactory" / jndiDestinationName="myOwnDestination" / jndiReplyDestinationName="myOwnReplyDestination" / connectionUserName="testUser" / connectionPassword="testPassword"> / <jms:JMSNamingProperty name="java.naming.factory.initial" / value="org.objectweb.celtix.transport.jms.MockInitialContextFactory"/> / <jms:JMSNamingProperty name="java.naming.provider.url" / value="tcp://localhost:61616"/> / </jms:address> / </value> / </property> / ... / </beans>

Text 4: Addressing Information in Celtix Configuration
More information
For more information on using Celtix configuration see the Celtix Configuration Guide.
# Consumer Endpoint Configuration
JMS consumer endpoints specify the type of messages they use. JMS consumer endpoint can use either a JMS ObjectMessage or a JMS TextMessage. When using an ObjectMessage the consumer endpoint uses a byte[] as the method for storing data into and retrieving data from the JMS message body. When messages are sent, the message data, including any formating information, is packaged into a byte[] and placed into the JMS message body before it is placed on the wire. When messages are received, the consumer endpoint will attempt to unmarshall the data stored in the JMS body as if it were packed in a byte[].
When using a TextMessage, the consumer endpoint uses a string as the method for storing and retrieving data from the JMS message body. When messages are sent, the message information, including any format-specific information, is converted into a string and placed into the JMS message body. When messages are received the consumer endpoint will attempt to unmashall the data stored in the JMS message body as if it were packed into a string.
When a native JMS applications interact with Celtix consumers, the JMS application is responsible for interpreting the message and the formatting information. For example, if the Celtix contract specifies that the binding used for a JMS endpoint is SOAP, and the messages are packaged as TextMessage, the receiving JMS application will get a text message containing all of the SOAP envelope information.
Consumer endpoint can be configured in one of two ways:
- Celtix configuration
- WSDL file
The recommended method is to place the consumer endpoint specific information into the Celtix configuration file for the endpoint.
## Using Celtix Configuration
Consumer endpoint configuration is specified using the org.objectweb.celtix.bus.transports.jms.jms_client_config.spring.JMSClientConfigBean class for the configuration bean. Using this configuration bean, you specify the message type supported by the consumer endpoint using the jmsClient property. It has a single value, jms:client, that has a single attribute:
messageType	Specifies how the message data will be packaged as a JMS message. text specifies that the data will be packaged as a TextMessage. binary specifies that the data will be packaged as an ObjectMessage.

Example
Text 5 shows a Celtix configuration entry for configuring a JMS consumer endpoint.
<beans xmlns:ct="http://celtix.objectweb.org/configuration/types" / xmlns:jms="http://celtix.objectweb.org/transports/jms"> / ... / <bean id="celtix.{http://celtix.objectweb.org/jms_conf_test} / HelloWorldQueueBinMsgService/HelloWorldQueueBinMsgPort.jms-client" / class="org.objectweb.celtix.bus.transports.jms.jms_client_config.spring.JMSClientConfigBean"> / <property name="jmsClient"> / <value> / <jms:client messageType="binary" /> / </value> / </property> / </bean> / ... / </beans>

Text 5: Configuration for a JMS consumer endpoint
Adding address information
In addition to specifying the jmsClient property, you can also specify the contact information used by the consumer for contacting a service endpoint. This is done by adding the jmsAddress property to the consumer endpoint's configuration bean.
More information
For more information on using Celtix configuration see the Celtix Configuration Guide.
## Using WSDL
The type of messages accepted by a JMS consumer endpoint is configured using the optional jms:client element. The jms:client element is a child of the WSDL port element and has one attribute:
messageType	Specifies how the message data will be packaged as a JMS message. text specifies that the data will be packaged as a TextMessage. binary specifies that the data will be packaged as an ObjectMessage.

# Service Endpoint Configuration
JMS service endpoints have a number of behaviors that are configurable in the contract. These include:
- how messages are correlated
- the use of durable subscriptions
- if the service uses local JMS transactions
- the message selectors used by the endpoint
Service endpoints can be configure in one of two ways:
- Celtix configuration
- WSDL file
## Using Celtix Configuration
Service endpoint configuration is specified using the org.objectweb.celtix.bus.transports.jms.jms_server_config.spring.JMSServerConfigBean class for the configuration bean. Using this configuration bean, you specify the service endpoint's behaviors using the jmsServer property. It has a single value, jms:server, that has a the following attributes:
useMessageIDAsCorrealationID	Specifies whether the JMS broker will use the message ID to correlate messages. The default is false.
durableSubscriberName	Specifies the name used to register a durable subscription.
messageSelector	Specifies the string value of a message selector to use. For more information on the syntax used to specify message selectors, see the JMS 1.1 specification.
transactional	Specifies whether the local JMS broker will create transactions around message processing. The default is false. Currently, this is not supported by the runtime.

Example
Text 6 shows a Celtix configuration entry for configuring a JMS service endpoint.
<beans xmlns:ct="http://celtix.objectweb.org/configuration/types" / xmlns:jms="http://celtix.objectweb.org/transports/jms"> / ... / <bean id="celtix.{http://celtix.objectweb.org/jms_conf_test} / HelloWorldQueueBinMsgService/HelloWorldQueueBinMsgPort.jms-server" / class="org.objectweb.celtix.bus.transports.jms.jms_server_config.spring.JMSServerConfigBean"> / <property name="jmsServer"> / <value> / <jms:server messageSelector="pickMe" / useMessageIDAsCorrelationID="true" / transactional="false" / durableSubscriberName="CeltixSubscriber" /> / </value> / </property> / </bean> / ... / </beans>

Text 6: Configuration for a JMS service endpoint
Adding address information
In addition to specifying the jmsServer property, you can also specify the contact information of the service endpoint. This is done by adding the jmsAddress property to the service endpoint's configuration bean.
More information
For more information on using Celtix configuration see the Celtix Configuration Guide.
## Using WSDL
Service endpoint behaviors are configured using the optional jms:server element. The jms:server element is a child of the WSDL port element and has the following attributes:
useMessageIDAsCorrealationID	Specifies whether JMS will use the message ID to correlate messages. The default is false.
durableSubscriberName	Specifies the name used to register a durable subscription.
messageSelector	Specifies the string value of a message selector to use. For more information on the syntax used to specify message selectors, see the JMS 1.1 specification.
transactional	Specifies whether the local JMS broker will create transactions around message processing. The default is false. Currently, this is not supported by the runtime.

# Using the JMS Context
The Celtix context mechanism can be used to inspect a number of the properties associated with a JMS message. The context mechanism can also be used to override some of the JMS endpoint's configuration.
## Inspecting JMS Properties
Once a message has been successfully retrieved from the JMS transport you can inspect the JMS header properties using the consumer's response context. In addition, you can see how long the client will wait for a response before timing out.
JMS Header Properties
The JMS properties table lists the properties in the JMS header that you can inspect. The JMS header properties are retrieved using the response context's get() method and supplying the value org.objectweb.celtix.jms.client.response.headers. The returned properties will be of type JMSMessageHeadersType.
Property Name	Property Type	Getter Method
Correlation ID	string	getJMSCorralationID()
Delivery Mode	int	getJMSDeliveryMode()
Message Expiration	long	getJMSExpiration()
Message ID	string	getJMSMessageID()
Priority	int	getJMSPriority()
Redelivered	boolean	getJMSRedlivered()
Time Stamp	long	getJMSTimeStamp()
Type	string	getJMSType()
Time To Live	long	getTimeToLive()

Table 1.: JMS Header Properties
In addition, you can inspect any optional properties stored in the JMS header using JMSMessageHeadersType.getPropery(). The optional properties are returned as a List of JMSPropertyType. Optional properties are stored as name/value pairs.
Client Receive Timeout
Celtix consumer endpoints have a JMS property control how long they will wait for a response before timing out. This property is stored as a long representing the number of milliseconds the consumer endpoint will wait for a response. To retrieve the property do the following:
1. Get the response context for the proxy you are using.
2. Retrieve the value by calling the response proxy's get() method with the value org.objectweb.celtix.jms.client.timeout.
Example
Text 7 shows code for inspecting some of the JSM properties using the response context.
// Proxy greeter initialized previously / InvocationHandler handler = Proxy.getInvocationHandler(greeter); / // Invoke on greeter proxy / BindingProvider bp= null; / if (handler instanceof BindingProvider) / { / bp = (BindingProvider)handler; / Map<String, Object> responseContext = bp.getResponseContext(); / JMSMessageHeadersType responseHdr = (JMSMessageHeadersType) / responseContext.get("org.objectweb.celtix.jms.client.response.headers"); / if (responseHdr != null) / { / System.out.println("Correlation ID: "+responseHdr.getJMSCorrelationID()); / System.out.println("Message Priority: "+responseHdr.getJMSPriority()); / System.out.println("Redelivered: "+responseHdr.getRedelivered()); / } / long clientTimeout = (long) / responseContext.get("org.objectweb.celtix.client.timeout"); / System.out.println("Client Receive Timeout: "+clientTimeout); / }

Text 7: Reading JMS Properties from the Response Context
The code in Text 7 does the following:
1. Gets the InvocationHandler for the proxy whose message headers you want to inspect.
2. Casts the returned InvocationHandler object into a BindingProvider object to retrieve the response context.
3. Gets the response context.
4. Retrieves the JMS message headers from the response context.
5. Prints some of the message header properties.
6. Retrieves the client receive timeout property from the response context.
7. Prints the client receive timeout property.
## Setting JMS Properties
Using the request context in a consumer endpoint, you can set a number of the JMS message header properties and the consumer endpoint's timeout value. These properties are valid for a single invocation. You will need to reset them each time you invoke an operation on the service proxy.
JMS Header Properties
The JMS properties table lists the properties in the JMS header that you can set using the consumer endpoint's request context.
Property Name	Property Type	Setter Method
Correlation ID	string	setJMSCorralationID()
Delivery Mode	int	setJMSDeliveryMode()
Time To Live	long	setTimeToLive()

Table 2.: Settable JMS Header Properties
To set these properties do the following:
1. Create a JMSMessageHeadersType object.
2. Populate the values you wish to set using the appropriate setter methods from the JMS properties table.
3. Set the values into the request context by calling the request context's put() method using org.objectweb.celtix.jms.client.request.headers as the first argument and the new JMSMessageHeadersType object as the second argument.
Optional JMS Header Properties
You can also set optional properties into the JMS header. Optional JMS header properties are stored in the JMSMessageHeadersType object that is used to set the other JMS header properties. They are stored as a List of JMSPropertyType. To add optional properties to the JMS header do the following:
1. Create a JMSPropertyType object.
2. Set the property's name field using setName().
3. Set the property's value field using setValue().
4. Add the property to the JMS message header to the JMS message header using JMSMessageHeadersType.getProperty().add(JMSPropertyType).
5. Repeat steps 1 through 4 until all of the properties have been added to the message header.
Client Receive Timeout
In addition to the JMS header properties, you can set the amount of time a consumer endpoint will wait for a response before timing out. You set the value by calling the request context's put() method with org.celtix.jms.client.timeout as the first argument and a long representing the amount of time in milliseconds that you want to consumer to wait as the second argument.
Example
Text 8 shows code for setting some of the JSM properties using the request context.
// Proxy greeter initialized previously / InvocationHandler handler = Proxy.getInvocationHandler(greeter); / BindingProvider bp= null; / if (handler instanceof BindingProvider) / { / bp = (BindingProvider)handler; / Map<String, Object> requestContext = bp.getRequestContext(); / JMSMessageHeadersType requestHdr = new JMSMessageHeadersType(); / requestHdr.setJMSCorrelationID("WithBob"); / requestHdr.setJMSExpiration(3600000L); / JMSPropertyType prop = new JMSPropertyType; / prop.setName("MyProperty"); / prop.setValue("Bluebird"); / requestHdr.getProperty().add(prop); / requestContext.put("org.objectweb.celtix.jms.client.request.headers", / requestHdr); / requestContext.put("org.objectweb.celtix.client.timeout", new Long(1000)); / }

Text 8: Setting JMS Properties using the Request Context
The code in Text 8 does the following:
1. Gets the InvocationHandler for the proxy whose JMS properties you want to change.
2. Casts the returned InvocationHandler object into a BindingProvider object to retrieve the request context.
3. Gets the request context.
4. Creates a JMSMessageHeadersType object to hold the new message header values.
5. Sets the Correlation ID.
6. Sets the Expiration property to 60 minutes.
7. Creates a new JMSPropertyType object.
8. Sets the values for the optional property.
9. Adds the optional property to the message header.
10. Sets the JMS message header values into the request context.
11. Sets the client receive timeout property to 1 second.